## Slide 1
FINAL PROGRESS REPORT
IoT Smart Watering
System
An automatic watering system using ESP32, soil moisture data, display monitoring, and pump control.
Presented by: Trần Quang Khả- 104240554
Vũ Xuân Tùng- 104240800
Notes: Good morning everyone. Today, I will present the final progress report of our IoT Smart Watering System project. The goal of this project is to create a simple automatic watering system that can monitor soil moisture and control a water pump based on the moisture condition.

## Slide 2
PROJECT OBJECTIVE
Main Objective
The purpose of this project is to build an IoT-based automatic watering system that can:
1
Read soil moisture data
2
Process the data using ESP32
3
Automatically activate the water pump when the soil is dry
4
Display soil moisture and pump status on a screen
5
Support future monitoring through Blynk dashboard
FINAL GOAL
Reduce manual watering and make plant care more automatic and convenient.
Automatic • Reliable • Convenient
IoT Smart Watering System
2 / 7
Notes: The main objective of our project is to reduce manual watering. The system reads soil moisture data, processes it with the ESP32, and controls the pump automatically. We also added a display so users can directly see the soil moisture value and the pump status.

## Slide 3
SYSTEM COMPONENTS
Hardware & Software
HARDWARE USED
ESP32 microcontroller
Soil moisture sensor
Relay module
Water pump
Display screen
Battery holder with ON/OFF switch
Voltage converter / power module
Jumper wires and connection cables
SOFTWARE / PLATFORM
Arduino IDE
ESP32 Wi-Fi connection
Live soil moisture readings
Blynk dashboard
IoT Smart Watering System
3 / 7
Notes: For the hardware, we used an ESP32 as the main controller. The soil moisture sensor is used to measure the moisture level. The relay controls the water pump. We also added a display screen to show the moisture value and the ON/OFF status. For power, we used a battery holder with a switch and connected it through a voltage converter to supply the ESP32 safely.

## Slide 4
SYSTEM WORKFLOW
How the System Works
1
Soil moisture data is received by the ESP32
2
ESP32 checks whether the soil is dry or wet
3
The moisture value is shown on the display
4
If the soil is dry, ESP32 activates the relay
5
The relay turns on the water pump
6
If the soil has enough moisture, the pump stays off
WORKFLOW DIAGRAM
Soil Moisture
Data
›
ESP32
Processing
›
Display
Monitoring
›
Relay
Control
›
Water Pump
ON / OFF
IoT Smart Watering System
4 / 7
Notes: The workflow of the system is simple. First, the ESP32 receives soil moisture data. Then, it compares the value with a threshold. If the soil is dry, the relay is activated and the pump turns on. If the soil is wet enough, the pump stays off. The display shows the current moisture value and the pump status so the user can monitor the system easily.

## Slide 5
COMPLETED FEATURES
What We Have Completed
✓
Connected all main components together
✓
Successfully controlled the water pump using ESP32
✓
Pump can turn ON/OFF based on moisture data
✓
Display can show moisture value
✓
Display can show pump/system status
✓
Battery switch can control system power
✓
System logic works with live soil moisture data
✓
Blynk dashboard connected for remote monitoring
IoT Smart Watering System
5 / 7
Notes: At this stage, most of the project has been completed. We connected the ESP32, relay, pump, display, power source, and other components together. The pump can be controlled based on moisture data, and the screen can display both the moisture value and the ON/OFF status. We have also connected the Blynk dashboard so the soil moisture and pump status can be monitored remotely. The system is able to demonstrate the main automatic watering logic.

## Slide 6
BLYNK DASHBOARD & FUTURE
Future Improvement
If the system is completed on time, we plan to send data to the Blynk dashboard.
DASHBOARD MAY SHOW
Soil moisture percentage
Pump status: ON / OFF
System status
Manual or automatic control option
FUTURE IMPROVEMENTS
Add water level sensor for the water tank
Improve the physical design of the control box
IoT Smart Watering System
6 / 7
Notes: For the final improvement, we may send the system data to the Blynk dashboard. This would allow users to monitor the soil moisture and pump status from a phone or computer. In the future, we also want to add a water level sensor for the tank and improve the design of the control box to make the project cleaner and more practical.

## Slide 7
CONCLUSION
Final Result
The IoT Smart Watering System can:
✓
Process soil moisture data
✓
Display moisture value and system status
✓
Control the water pump automatically
✓
Demonstrate smart watering logic
✓
Support future IoT dashboard monitoring
CONCLUSION
With the soil moisture sensor now working reliably, the main system logic is fully functional.
The project successfully demonstrates an automatic watering system using ESP32, relay control, display monitoring, and pump activation.
IoT Smart Watering System
7 / 7
Notes: In conclusion, our project successfully demonstrates the main idea of an IoT automatic watering system. The ESP32 can process moisture data, display the value, and control the pump automatically. The soil moisture sensor is now working reliably, the system logic is working correctly, and the project is almost complete.